## Slide 1: Adder

## Slide 2: آزمون ميان ترم
چهارشنبه 5 آذر، ساعت 12 تا 13:30
کتبی: مودل + نیما
شفاهی: اسکایپ یا نیما

## Slide 3: Half Adder (HA)
  Add single bits
Ai
0
0
1
1
Bi
0
1
0
1
Sum
0
1
1
0
Carry
0
0
0
1

## Slide 4: Half Adder (HA)
  Add single bits
Ai
0
0
1
1
Bi
0
1
0
1
Sum
0
1
1
0
Carry
0
0
0
1
Ai
Bi
0
1
0
1
0
1
1
0
Sum = Ai Bi + Ai Bi
= AiBi
Ai
Bi
0
1
0
1
0
0
1
0
Carry = Ai . Bi

## Slide 5: Full Adder
  Add multiple bits

## Slide 6: Full Adder (FA)
S = CI xor A xor B
CO = B CI + A CI + A B = CI (A + B) + A B
A
0
0
0
0
1
1
1
1
B
0
0
1
1
0
0
1
1
CI
0
1
0
1
0
1
0
1
S
0
1
1
0
1
0
0
1
CO
0
0
0
1
0
1
1
1
A B
CI
0
1
00
01
11
10
0
1
1
0
1
0
0
1
A B
CI
0
1
00
01
11
10
0
0
0
1
0
1
1
1
S
CO

## Slide 7: Full Adder Using 2 Half Adders
  A full adder can also be realized with two half adders and an OR gate, since Ci+1 can also be expressed as:
  Ci+1 = AiBi + (Ai  Bi)Ci
  and Si = (Ai  Bi)  Ci
Ai
Bi
Ci
Ci+1
Si

## Slide 8: Example: 4-bit Ripple Carry Adder
C4 C3 C2 C1 C0 A3 A2 A1 A0 +B3 B2 B1 B0 -------------- S3 S2 S1 S0

## Slide 9: Delay Analysis of Ripple Adder
  Carry out of a single stage can be implemented in 2 gate delays after CI is ready.
  For a 16 bit adder, the 16th bit carry is generated after about 16 * 2 = 32 gate delays.
  The sum bit takes one additional gate delay to generate the sum of the 16th bit after 15th bit carry
    ~ 15 * 2 + 1 = 31 gate delays
  Takes too long - need to investigate FASTER adders!
A
A
A
B
B
B
CI
CI
S
CO

## Slide 10: Ripple Carry Adder Delay Analysis
A
A
B
B
CI
CO
@0
@0
@0
@0
@t
@1
@1
@t+1
@t+2
late
arriving
signal
A
B
CI
S
@0
@0
@t
@t+1

## Slide 11: Ripple Carry Adder Delay Analysis
@0
@0
@0
A
A
B
B
CI
CO
@0
@0
@0
@0
@t
@1
@1
@t+1
@t+2
late
arriving
signal
@2
@3
@0
@0
@0
@0
@0
@0
@5
@4
@7
@9
A
B
CI
S
@0
@0
@t
@t+1

## Slide 12: Carry Lookahead Adder
Carry Generate
  Gi = Ai Bi must generate carry when A = B = 1
Carry Propagate
  Pi = Ai xor Bi carry-in will equal carry-out here
Sum and Carry can be reexpressed in terms of generate/propagate:
Si = Ai xor Bi xor Ci = Pi xor Ci
Ci+1 = Ai Bi + Ai Ci + Bi Ci
= Ai Bi + Ci (Ai + Bi)
= Ai Bi + Ci (Ai xor Bi)
= Gi + Ci Pi

## Slide 13: Carry Lookahead Adder
C1 = G0 + P0 C0
C2 = G1 + P1 C1
= G1 + P1 (G0 + P0 C0)
= G1 + P1 G0 + P1 P0 C0
C3 = G2 + P2 C2
= G2 + P2 (G1 + P1 G0 + P1 P0 C0)
= G2 + P2 G1 + P2 P1 G0 + P2 P1 P0 C0
C4 = G3 + P3 C3
= G3 + P3 G2 + P3 P2 G1 + P3 P2 P1 G0 + P3 P2 P1 P0 C0
  Each of the carry equations can be implemented in a two-level logic network
  Variables are the adder inputs and carry in to stage 0!

## Slide 14: CLA
  Increasingly complex logic
Pi
Ci
Si
Bi
Ai
Gi
C0
P0
G0
C1
C0
P0
G0
P1
P1
G1
C2
C0
P0
G0
P1
P1
G1
P2
P2
P2
G2
C3
C0
P0
G0
P1
P1
G1
P2
P2
P2
G2
P3
P3
P3
P3
G3
C4
@0
@0
@t
@1
@t+1
@1

## Slide 15: Ripple Carry Adder Delay Analysis
@0
@0
@0
@2
@3
@0
@0
@0
@0
@0
@0
@3
@4
@3
@3
Pi
Ci
Si
Bi
Ai
Gi
@0
@0
@t
@1
@t+1
@1
C0
P0
G0
P1
P1
G1
P2
P2
P2
G2
C3
@4
@4
@1
@0

## Slide 16: Delay Analysis of CLA
  NOTE: This assumes all gate delay are same.
  Not true, delays depend on fan-ins and fan-out

## Slide 17: Cascaded CLA
CLA
CLA
CLA

## Slide 18: Adder/Subtractor
A - B = A + (-B) = A + B’ + 1
A
B
CO
S
+
CI
A
B
CO
S
+
CI
A
B
CO
S
+
CI
A
B
CO
S
+
CI
Add/Subtract
A
3
B
3
A
2
B
2
A
1
B
1
A
0
B
0
S
3
S
2
S
1
S
0
Overflow

## Slide 19: Adder/Subtractor
A - B = A + (-B) = A + B’ + 1

## Slide 20: 4-bit Binary Adder/Subtractor (cont.)
S=0
0
B0
S=0 selects addition
B1
B2
B3

## Slide 21: 4-bit Binary Adder/Subtractor (cont.)
S=1
1
B0’
S=1 selects subtraction
B1’
B2’
B3’

## Slide 22: Overflow
  Overflow can occur ONLY when both numbers have the same sign.
  This condition can be detected when the carry out (Cn) is different than the carry at the previous position (Cn-1).

## Slide 23: The Overflow problem in Signed-2’s Complement (cont.)
Example 1: M=6510 and N=6510 (In an 8-bit 2’s complement system).
  M = N = 010000012
  M+N = 10000010 with Cn=0. (clearly wrong!)
  Bring Cn as the MSB to get 0100000102 (13010) which is correct, but requires 9-bits  overflow occurs.
Example 2: M=-6510 and N=-6510
  M = N = 101111112
  M+N = 01111110 with Cn=1. (wrong again!)
  Bring Cn as the MSB to get 1011111102 (-13010) which is correct, but also requires 9-bits  overflow occurs.

## Slide 24: Overflow Detection in Signed-2’s Complement
n-bit Adder/Subtractor
V
C
Cn
Cn-1
C =1 indicates overflow condition when adding/subtr. unsigned numbers.
V=1 indicates overflow condition when adding/subtr. signed-2’s complement numbers

## Slide 25: 2x2-bit Multiplier
4-variable K-map
for each of the 4
output functions
A2 A1 B2 B1 P8 P4 P2 P1
0 0 0 0 0 0 0 0
0 1 0 0 0 0
1 0 0 0 0 0
1 1 0 0 0 0
0 1 0 0 0 0 0 0
0 1 0 0 0 1
1 0 0 0 1 0
1 1 0 0 1 1
1 0 0 0 0 0 0 0
0 1 0 0 1 0
1 0 0 1 0 0
1 1 0 1 1 0
1 1 0 0 0 0 0 0
0 1 0 0 1 1 1 0 0 1 1 0
1 1 1 0 0 1
P1
P2 P4
P8
A1
A2 B1
B2

## Slide 26: 2x2-bit Multiplier (cont’d)
K-map for P8
K-map for P4
K-map for P2
K-map for P1
0 0
0 0
0 0
0 0
B1
A2
0 0
0 0
0 1
1 1
A1
B2
0 0
0 1
0 0
1 0
B1
A2
0 1
0 0
1 0
0 0
A1
B2
0 0
0 0
0 0
1 1
B1
A2
0 1
0 1
0 1
1 0
A1
B2
0 0
0 0
0 0
0 0
B1
A2
0 0
0 0
1 0
0 0
A1
B2
P8 = A2A1B2B1
P4 = A2B2B1' + A2A1'B2
P2 = A2'A1B2 + A1B2B1' + A2B2'B1 + A2A1'B1
P1 = A1B1

## Slide 27: Multiplier
Y0
X0
Y0
X0 Y0
X1
Y1
X1 Y0
X0 Y1
X2
Y2
X2 Y0
X1 Y1
X0 Y2
X3
Y3
X2 Y0
X2 Y1
X1 Y2
X0 Y3
X3 Y1
X2 Y2
X1 Y3
X3 Y2
X2 Y3
X3 Y3
Z6
Z5
Z4
Z3
Z2
Z1
Z0
Z7

## Slide 28: 4-Bit ALU
74181 TTL ALU
  Arithmetic-Logic Unit

## Slide 29: 4-Bit ALU

## Slide 30: BCD Addition
Addition:
5 = 0101
3 = 0011
1000 = 8
5 = 0101
8 = 1000
1101 = 13!
Problem
when digit
sum exceeds 9
Solution: add 6 (0110) if sum exceeds 9!
5 = 0101
8 = 1000
1101
6 = 0110
1 0011 = 1 3 in BCD
9 = 1001
7 = 0111
1 0000 = 16 in binary
6 = 0110
1 0110 = 1 6 in BCD

## Slide 31: اعداد در مبناهاي مختلف
Add 0110 to sum whenever it exceeds 1001 (11XX or 1X1X)

## Slide 32: BCD Adder
Add 0110 to sum whenever it exceeds 1001 (11XX or 1X1X)
F
A
F
A
F
A
F
A
Cin
A
3
A
2
A
1
A
0
B
3
B
2
B
1
B
0
Cout
S
3
S
2
S
1
S
0
CO
CI
S
CO
CI
S
CO
CI
S
CO
CI
S

## Slide 33: BCD Adder
Add 0110 to sum whenever it exceeds 1001 (11XX or 1X1X)
F
A
F
A
F
A
F
A
F
A
F
A
Cin
A
3
A
2
A
1
A
0
B
3
B
2
B
1
B
0
Cout
S
3
S
2
S
1
S
0
0
CO
CI
S
CO
CI
S
CO
CI
S
CO
CI
S
CO
CI
S
CO
CI
S
1
1XX
A1
A2
1X1X