## Slide 1: Sequential Circuit Analysis

## Slide 2: Synchronous vs. Asynch.
Synchronous sequential circuit:
  Behavior: from knowledge of its signals at discrete instants of time.
  Synchronization by a signal: clock
Asynchronous sequential circuit:
  Behavior: dependent on the order of input signal changes over continuous time
  Output can change at any time (clockless).

## Slide 3: Clock Signal
Different duty cycles
Clock generator: Periodic train of clock pulses
Rising Clock Edge
Falling Clock Edge

## Slide 4: Clock Signal
  Clock is distributed throughout the whole design
  Each component synchronizes itself with it.

## Slide 5: Synchronous Circuits
Combinational
Logic
time
clk

## Slide 6: Synchronous Circuits
Combinational
Logic
time
clk

## Slide 7: Synchronous Circuits
Combinational
Logic
time
clk

## Slide 8: Synchronous Circuits
Combinational
Logic
time
clk

## Slide 9: Sequential Circuit Analysis
Analysis:
  Obtaining a suitable description that demonstrates the time sequence of inputs, outputs, and states.

## Slide 10: Sequential Circuits
  At each clock period, the present state of the system is stored in storage elements (FFs)

## Slide 11: Example 1
Input: x(t)
Output: y(t)
State: (A(t), B(t))
What is the Output Function?
What is the Next State Function?
A
C
D
Q
Q
C
D
Q
Q
y
x
A
B
CP

## Slide 12: Example 1 (Cont’d)
Boolean equations for the functions:
  A(t+1) = A(t)x(t) + B(t)x(t)
  B(t+1) = A’(t)x(t)
  y(t) = x’(t)(B(t) + A(t))
C
D
Q
Q
C
D
Q
Q'
y
x
A
A’
B
CP
Next State
Output

## Slide 13: Example 1 (Cont’d)
0
0
0
0
1
1
1
0
A(t+1)
B(t+1)
Has error?
  A(t+1) = A(t)x(t) + B(t)x(t)
  B(t+1) = A’(t)x(t)
  y(t) = x’(t)(B(t) + A(t))
A(t), B(t)
A(t), B(t)
A(t+1), B(t+1)
A(t)
B(t)

## Slide 14: Example 1 (Cont’d)
0
0
0
0
1
1
1
0
A(t+1)
B(t+1)
Has error?
  A(t+1) = A(t)x(t) + B(t)x(t)
  B(t+1) = A’(t)x(t)
  y(t) = x’(t)(B(t) + A(t))
A(t), B(t)
A(t), B(t)
A(t+1), B(t+1)
A(t)
B(t)

## Slide 15: State Table Characteristics
State table
  A multiple variable table with the following four sections:
  Present State:
    the values of the state variables for each allowed state.
  Input:
    the input combinations allowed.
  Next-state:
    the value of the state at time (t+1) based on the present state and the input.
  Output:
    the value of the output as a function of the present state and (sometimes) the input.
A(t), B(t)
A(t), B(t)
A(t+1), B(t+1)

## Slide 16: State Table Characteristics
From the viewpoint of a truth table:
  TT inputs:
    Input, Present State
  TT outputs:
    Output, Next State

## Slide 17: State Table
Example:
  The state table can be filled in using the next state and output equations:
    A(t+1) = A(t)x(t) + B(t)x(t)
    B(t+1) =A (t)x(t)
    y(t) =x (t)(B(t) + A(t))
Present State
Input
Next State
Output
A(t) B(t)
x(t)
A(t+1) B(t+1)
y(t)
0 0
0
0 0
0
0 0
1
0 1
0
0 1
0
0 0
1
0 1
1
1 1
0
1 0
0
0 0
1
1 0
1
1 0
0
1 1
0
0 0
1
1
1
1
1 0
0

## Slide 18: State Diagram
  The sequential circuit function can be represented in graphical form as a state diagram with the following components:
    Circles (state name inside): states
    Directed arcs: Present State Next State: state transition
    label on each arc with the Input values which causes the state transition, and
    A label for the output:
      on each directed arc, or
      on each circle
I/O
S1
S2
I
S1/O1
S2/O2

## Slide 19: Mealy vs. Moore machines
Mealy model:
  Both outputs and next state depend both on primary inputs AND present state.
    Next_state = f(inputs, state)
    Out = g(inputs, state)
Moore model:
  Only next state depends directly on primary inputs AND present state. Outputs depend only on present state.
    Next_state = f(inputs, state)
    Out = g(state)

## Slide 20: State Diagram
Label form:
  Mealy:
    On directed arc :
        inputs/outputs
    In circle:
        State name
  Moore:
    On directed arc:
      Inputs
    In circle:
      state/output
    Mealy:
      output g(state, input)
    Moore:
      output g(state)

## Slide 21: Example: Mealy model (cont.)
State Diagram
00
0/0
01
1/0
0/1
11
1/0
0/1
10
1/0
0/1
1/0
I/O
S1
S2
Reads as: When at state s1 and apply
input I, we get output O
and proceed to state s2.

## Slide 22: Example: Moore model (cont.)
I
S1/O1
S2/O2
Reads as: When at state s1 with output
O1 and apply input I,
we proceed to state s2 with
Output O2.
State Diagram
0/0
00
1/1
10
10
11
11
00
01
01

## Slide 23: Example: Moore model (cont.)
I
S1/O1
S2/O2
Reads as: When at state s1 with output
O1 and apply input I,
we proceed to state s2 with
Output O2.
0/0
00,11
1/1
01,10
01,10
00,11
State Diagram
0/0
00
1/1
10
10
11
11
00
01
01

## Slide 24: State Diagram
  Which type?
A B
0 0
0 1
1 1
1 0
x=0/y=1
x=1/y=0
x=1/y=0
x=1/y=0
x=0/y=1
x=0/y=1
x=1/y=0
x=0/y=0

## Slide 25: General Sequential Circuit

## Slide 26: Mealy Machine
State Register
C1
x(t)
s(t+1)
s(t)
z(t)
clock
present
state
present
inputs
next
state
C2

## Slide 27: Moore Machine
State Register
C1
x(t)
s(t+1)
s(t)
z(t)
clock
present
state
present
inputs
next
state
C2

## Slide 28: Example of a M…? machine
Obtain the logic diagram and state table for:
  DA = A  X  Y
  Z = A

## Slide 29: Example of a M…? machine
Obtain the logic diagram and state table for:
  DA = A  X  Y
  Z = A
D
C
clock
X
Y
A
Z
DA

## Slide 30: Example of a Moore Machine (cont.)
Present State | Inputs |  | Next State | Output
A(t) | X | Y | A(t+1) | Z
D
C
clock
X
Y
A
Z
DA
State Table

## Slide 31: Example of a Moore Machine (cont.)
Present State | Inputs |  | Next State | Output
A(t) | X | Y | A(t+1) | Z
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
D
C
clock
X
Y
A
Z
DA
State Table

## Slide 32: Example of a Moore Machine (cont.)
Present State | Inputs |  | Next State | Output
A(t) | X | Y | A(t+1) | Z
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
Present State | Next State |  |  |  | Output
 | XY=00 | XY=01 | XY=10 | XY=11 | 
A(t) | A(t+1) | A(t+1) | A(t+1) | A(t+1) | Z
0 | 0 | 1 | 1 | 0 | 0
1 | 1 | 0 | 0 | 1 | 1
D
C
clock
X
Y
A
Z
DA
State Table
Alternative State Table

## Slide 33: Example: Mealy model
State Table
Possible states = { 00, 01, 10, 11 }
 4 nodes in state diagram
Y = (A+B).X’
A(t+1) = (A+B).X
B(t+1) = A’.X
Present State |  | Input | Next State |  | Output
A(t) | B(t) | X | A(t+1) | B(t+1) | Y
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1
1 | 1 | 1 | 1 | 0 | 0

## Slide 34: Example: Mealy model (cont.)
State Diagram
00
0/0
01
1/0
0/1
11
1/0
0/1
10
1/0
0/1
1/0
Present State |  | Input | Next State |  | Output
A(t) | B(t) | X | A(t+1) | B(t+1) | Y
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1
1 | 1 | 1 | 1 | 0 | 0

## Slide 35: Example: Moore model
State Table
Possible states = { 0, 1 }
 2 nodes in state diagram
Present State | Inputs |  | Next State | Output
A(t) | X | Y | A(t+1) | Z
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 36: Example: Moore model (cont.)
State Diagram
0/0
00,11
1/1
01,10
01,10
00,11
Present State | Inputs |  | Next State | Output
A(t) | X | Y | A(t+1) | Z
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 37: State Tables for Other Flip-Flops
Two step procedure:
  Obtain binary values of each FF input equation in terms of present state and input variables.
  Use corresponding FF characteristic table to determine the next state.

## Slide 38: Example
  JA = B, KA = BX’
  JB = X’, KB = AX’ + A’X = A  X
 2 JK-FFs:
J
K
C
J
K
C
JA
KA
KB
JB
A
A’
B
B’
J | K | Q(t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | Q(t)’
JK-FF Characteristic Table
38
JK-FF Characteristic Table

## Slide 39: Example (cont.)
Present State |  | Input | Next State |  | FF inputs |  |  | 
A(t) | B(t) | X | A(t+1) | B(t+1) | JA | KA | JB | KB
0 | 0 | 0 |  |  | 0 | 0 | 1 | 0
0 | 0 | 1 |  |  | 0 | 0 | 0 | 1
0 | 1 | 0 |  |  | 1 | 1 | 1 | 0
0 | 1 | 1 |  |  | 1 | 0 | 0 | 1
1 | 0 | 0 |  |  | 0 | 0 | 1 | 1
1 | 0 | 1 |  |  | 0 | 0 | 0 | 0
1 | 1 | 0 |  |  | 1 | 1 | 1 | 1
1 | 1 | 1 |  |  | 1 | 0 | 0 | 0
Step 1: Use FF input equations
  JA = B, KA = BX’
  JB = X’, KB = AX’ + A’X = A  X

## Slide 40: Example (cont.)
Present State |  | Input | Next State |  | FF inputs |  |  | 
A(t) | B(t) | X | A(t+1) | B(t+1) | JA | KA | JB | KB
0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0
0 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0
Step 2: Use FF inputs and JK characteristic table

## Slide 41: Example 2: Sequential Circuit Analysis
  Logic Diagram:
Clock
Reset
D
Q
C
Q
R
D
Q
C
Q
R
D
Q
C
Q
R
A
B
C
Z

## Slide 42: Example 2: Flip-Flop Input Equations
Variables
  Inputs: None
  Outputs: Z
  State Variables: A, B, C
Initialization:
  Reset to (0,0,0)
Equations
  A(t+1) = Z =
  B(t+1) =
  C(t+1) =
Mealy or Moore?
Notes: A(t+1) = BC
B(t+1) = B’C + BC’
C(t+1) = A’C’
Z = A

## Slide 43: Example 2: State Table
A B C | A+B+C+ | Z
0 0 0 |  | 
0 0 1 |  | 
0 1 0 |  | 
0 1 1 |  | 
1 0 0 |  | 
1 0 1 |  | 
1 1 0 |  | 
1 1 1 |  | 
S+=S(t+1)
Notes: A’B’C’: 0 0 1, 0 1 0, 0 1 1, 1 0 0, 0 0 0, 0 1 0, 0 1 0, 1 0 0
Z: 0 0 0 0 1 1 1 1

## Slide 44: Example 2: State Diagram
Which states are used?
What is the function of the circuit?
000
011
010
001
100
101
110
111
Reset
ABC
Notes: Only states reachable from the reset state 000 are used: 000, 001, 010, 011, and 100.
The circuit produces a 1 on Z after four clock periods and every five clock periods thereafter:
000 -> 001 -> 010 -> 011 -> 100 -> 000 -> 001 -> 010 -> 011 -> 100 …
1 1

## Slide 45: Example 3
Mealy or Moore?
Present
Output(Z)
Next state
Present
State
00 01 11 10 | 01 00 11 01 11 11 01 | 0 1 0 1 | 

## Slide 46: Example 3
Present State | Next state | Present Output(Z)

## Slide 47: Example 4
  Mealy or Moore?
0 1
1 0
0 1
0 1
00 01
01 11
11 00
10 01
00
01
11
10
Present
Output(z)
Next state
Present
State

## Slide 48: Example 4
Present State | Next state | Present Output(z)

## Slide 49: Circuit Analysis by Signal Tracing
Waveforms

## Slide 50: Timing Chart
Construction and interpretation of Timing Chart:
  A state change can only occur after the rising (or falling) edge of the clock.
  The input will normally be stable immediately before and after the active clock edge.
  For a Mealy circuit, the output can change when the input changes as well as when the state changes.
    A false output may occur between the state changes and the time the input is changed to its new value. (In other words, if the state has changed to its next value, but the old input is still present, the output may be temporarily incorrect.)
  False outputs are difficult to determine from the state graph, so use signal tracing.

## Slide 51: Timing Charts
  Timing chart plotting procedure for Mealy state table :
    For the given input value, read the present output and plot it.
      If the input changes many times before clock edge, plot the effects on output.
    After the active clock edge, change the present state according to the next state function.
    Any change in present state may cause change in next state and output.
    Repeat steps (a) and (b).
  For Mealy circuits, the best time to read the output is just before the active edge of the clock, because the output should always be correct at that time.

## Slide 52: Example
Timing Chart for a Mealy Machine
X = 1 0 1 0 1
A = 0 0 0 1 1 0
B = 0 1 1 1 1 0
Z = 1(0) 1 0(1) 0 1
(False outputs are indicated in parentheses)

## Slide 53: Example

## Slide 54: Example: Serial Adder
xi yi ci | ci+1 si
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | 0 0 0 1 0 1 1 0 0 1 1 0 1 0 1 0
(b) Truth table

## Slide 55: Serial Adder
State Diagram
S0: Q = 0
S1: Q = 1

## Slide 56: Serial Adder Timing Diagram
  Si can be read before the rising edge of Clock
    At 2nd clock: Xi=Yi=1, Ci=0  Si=0
      But after clock, Ci changes, but old Xi
       Si changes to a wrong value.
10011 xi
00110 yi

## Slide 57: State Tables
A State table with Multiple Inputs and Outputs
Present State | Next state | Present Outputs

## Slide 58: State Diagram
A State Diagram with Multiple Inputs and Outputs

## Slide 59: Mealy Machine State Diagrams
A CLARIFICATION:
  The state-diagram notation for output values in Mealy machines is a little misleading:
    You should remember that the listed output value is produced continuously when the machine is in the indicated state and has the indicated input, (not just during the transition to the next state).