## Slide 1: Registers and Counters

## Slide 2: Overview
Parallel Load Register
Shift Registers
  Serial Load
  Serial Addition
Shift Register with Parallel Load
Bidirectional Shift Register

## Slide 3: Registers and Counters
An n-bit register
  n flip-flops
  Capable of storing n bits of binary information.
Counter:
  FSM that goes through a predetermined sequence of states

## Slide 4: 4-Bit Register
Load

## Slide 5: Register with parallel load

## Slide 6: Shift Register
0
1
0
0
1

## Slide 7: Shift Register
Output SO
0
1
0
0
1

## Slide 8: Serial data transfer
Serial transfer of information from register A to register B

## Slide 9: Serial addition using shift registers
The two binary numbers to be added serially are stored in two shift registers.
The sum bit on the S output of the full adder is transferred into the result register A.

## Slide 10: Serial vs. parallel addition
  Inputs come from a shift register
  Outputs are saved in a shift register

## Slide 11: Shift register with parallel load
Shift | Load | Operation
0 | 0 | Nothing
0 | 1 | Load parallel
1 | X | Shift Q0  Q1, Q1Q2…

## Slide 12: Shift register with parallel load

## Slide 13: Bidirectional shift register
S1S0 | Action
00 | Nothing
01 | Shift down
10 | Shift up
11 | Parallel load

## Slide 14: Bidirectional Shift Register

## Slide 15: Counters
Counter
  A predetermined sequence of states with each clock
  Synchronous Counter: - All FFs receive a common clock
  Ripple Counter: - FF output transition serves as a source for triggering other FFs.
  - No common clock

## Slide 16: Synchronous Binary Counters
Design procedure
  Like other synchronous sequential circuits
  Most efficient implementations: by T or JK
    We will examine JK and D flip-flop designs

## Slide 17
J-K Flip Flop Design of a 4-bit Binary Up Counter
Synchronous Binary Counters:

## Slide 18
J-K Flip Flop Design of a 4-bit Binary Up Counter
Synchronous Binary Counters:

## Slide 19
J-K Flip Flop Design of a Binary Up Counter (cont.)
Synchronous Binary Counters

## Slide 20
J-K Flip Flop Design of a Binary Up Counter (cont.)
Synchronous Binary Counters

## Slide 21
J-K Flip Flop Design of a Binary Up Counter (cont.)
Synchronous Binary Counters

## Slide 22
J-K Flip Flop Design of a Binary Up Counter (cont.)
Synchronous Binary Counters
JQ0 = 1
KQ0 = 1
JQ1 = Q0
KQ1 = Q0
JQ2 = Q0 Q1
KQ2 = Q0 Q1
JQ3 = Q0 Q1 Q2
KQ3 = Q0 Q1 Q2
J
K
C
J
K
C
J
K
C
J
K
C
CLK
logic 1
Q0
Q1
Q2
Q3

## Slide 23
J-K Flip Flop Design of a Binary Up Counter with EN and CO
Synchronous Binary Counters:
EN = enable control signal, when 0 counter remains in the same state, when 1 it counts
CO = carry output signal, used to extend the counter to more stages
JQ0 = 1 · EN
KQ0 = 1 · EN
JQ1 = Q0 · EN
KQ1 = Q0 · EN
JQ2 = Q0 Q1 · EN
KQ2 = Q0 Q1 · EN
JQ3 = Q0 Q1 Q2 · EN
KQ3 = Q0 Q1 Q2 · EN
C0 = Q0 Q1 Q2 Q3 · EN

## Slide 24
4-bit Upward Synchronous Binary
Counter in HDL - Simulation

## Slide 25: Synchronous Binary Counter Using DFF

## Slide 26: Counter with Parallel Load
Add path for input data
  enabled for Load = 1
Add logic to:
  disable count logic for Load = 1
  disable feedback from outputs for Load = 1
  enable count logic for Load = 0 and Count = 1
The resulting function table:
D
0
D
C
Q
0
D
1
D
C
Q
1
D
2
D
C
Q
2
D
3
D
C
Q
3
Load
Count
Clock
Carry
Output CO
Load | Count | Action
0 | 0 | Hold Stored Value
0 | 1 | Count Up Stored Value
1 | X | Load D

## Slide 27: Counting Modulo 7: Detect 7 and Asynchronously Clear
A synchronous 4-bit binary counter with an asynchronous Clear is used to make a Modulo 7 counter.
Use the Clear feature to detect the count 7 and clear the count to 0. This gives a count of 0, 1, 2, 3, 4, 5, 6, 7(short)0, 1, 2, 3, 4, 5, 6, 7(short)0, etc.
Clock
0
D3
Q3
D2
Q2
D1
Q1
D0
Q0
CLEAR
CP
LOAD

## Slide 28: Counting Modulo 7: Detect 7 and Asynchronously Clear
A synchronous 4-bit binary counter with an asynchronous Clear is used to make a Modulo 7 counter.
Use the Clear feature to detect the count 7 and clear the count to 0. This gives a count of 0, 1, 2, 3, 4, 5, 6, 7(short)0, 1, 2, 3, 4, 5, 6, 7(short)0, etc.
DON’T DO THIS! Referred to as a “suicide” counter! (Count “7” is “killed,” but the designer’s job may be dead as well!)
Clock
0
D3
Q3
D2
Q2
D1
Q1
D0
Q0
CLEAR
CP
LOAD

## Slide 29: Modulo 7 Counter
A synchronous binary counter
Synchronous load
Asynchronous clear
Uses Load to detect "6" and load in "zero".
Counts: 0, 1, 2, 3, 4, 5, 6, 0, 1, 2, 3, 4, 5, 6, 0, ...
Using don’t cares for states > 0110
D3
Q3
D2
Q2
D1
Q1
D0
Q0
CLEAR
CP
LOAD
Clock
0
0
0
0
Reset

## Slide 30: Modulo 6 Counter Starting from 9
Synchronous counter
Uses synchronous Load to preset to 9 on Reset and detection of 14.
Count 9, 10, 11, 12, 13, 14, 9, 10, 11, 12, 13, 14, 9, …
Clock
D3
Q3
D2
Q2
D1
Q1
D0
Q0
CLEAR
CP
LOAD
0
0
1
1
Reset
1

## Slide 31: Ripple Counter
How does it work?
  A positive edge on clock input of A  A complements
  Clock input of B = Q’ of flip-flop A
  When A changes from 1 to 0  positive edge on the clock input of B  B is complemented
Reset
Clock
D
D
Q’
B
A
CP
B
A
0
1
2
3
0
1
Q’
Q
Q

## Slide 32: Example (cont.)

## Slide 33: Ripple Counter (continued)
The arrows show the cause-effect relation- ship from the prior slide =>
The corresponding sequence of states => (B,A) = (0,0),
Each additional bit, C, D, …behaves like bit B, changing half as frequently as the bit before it.
For 3 bits: (C,B,A) = (0,0,0), (0,0,1), (0,1,0), (0,1,1), (1,0,0), (1,0,1), (1,1,0), (1,1,1), (0,0,0), …
(1,0),
(0,1),
(0,1), …
(0,0),
(1,1),
CP
B
A
0
1
2
3
0
1

## Slide 34: Ripple Counter (continued)
Starting with C = B = A = 1, equivalent to (C,B,A) = 7, the next clock increments the count to (C,B,A) = 0. In fine timing detail:
  The clock to output delay tPHL causes an increasing delay from clock edge for each stage transition.
  Thus, the count “ripples” from least to most significant bit.
  For n bits, total worst case delay is n tPHL.
CP
A
B
C
tPHL
tPHL
tpHL

## Slide 35: Example: A 4-bit Upward Counting Ripple Counter
Recall...
Less Significant
Bit output is Clock
for Next Significant Bit!
(Clock is active low)

## Slide 36: A 4-bit Downward Counting Ripple Counter
  Use direct Set (S) signals instead of direct Reset (R), in order to start at 1111.
  Change edge-triggering to positive
Alternative designs:
  Connect the complement output of each FF to the C input of the next FF in the sequence.

## Slide 37
Simulation …