## Slide 1: Programmable Logic
PAL, PLA

## Slide 2: PLAs
Programmable Logic Array
  Pre-fabricated building block of many AND/OR gates (or NOR, NAND)
  General purpose logic building blocks
  “Personalized” or “customized” by making/ breaking connections among the gates
  This process is called “programming”

## Slide 3: PLA
Realizes Sums of Products

## Slide 4: PLA

## Slide 5: PLA
A 3×2 PLA with 4 product terms.

## Slide 6: Design for PLA: Example
  Implement the following functions using PLA
F0 = A + B' C'
F1 = A C' + A B
F2 = B' C' + A B
F3 = B' C + A
Personality Matrix
1 = asserted in term
0 = negated in term
- = does not participate
Input Side:
1 = term connected to output
0 = no connection to output
Output Side:
Outputs
Inputs
Product
t
erm
A
1
-
1
-
1
B
1
0
-
0
-
C
-
1
0
0
-
F
0
0
0
0
1
1
F
1
1
0
1
0
0
F
2
1
0
0
1
0
F
3
0
1
0
0
1
A B
B C
A C
B C
A

## Slide 7: Example: Continued
F0 = A + B' C'
F1 = A C' + A B
F2 = B' C' + A B
F3 = B' C + A
A
B
C
F0
F1
F2
F3
AB
B’C
AC’
B’C’
A

## Slide 8: Constants
  Sometimes a PLA output must be programmed to be a constant 1 or a constant 0.
  Manufacturer MAY “pull up” the AND inputs:
    P1 is always 1 because its product line is connected to no inputs and is therefore always pulled UP or HIGH.
    This constant 1 term drives the O1 output.
  Manufacturer MAY “pull down” the OR inputs:
    No product term drives the O2 output, which is therefore always 0.
  Another method of obtaining a constant-0 output is shown for O3.

## Slide 9: Gray Codes
Gray codes are minimum change codes
  From one numeric representation to the next, only one bit changes

## Slide 10: Gray Codes (cont.)
Binary
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Gray
0000
0001
0011
0010
0110
0111
0101
0100
1100
1101
1111
1110
1010
1011
1001
1000
Binary
00
01
10
11
Gray
00
01
11
10
Binary
000
001
010
011
100
101
110
111
Gray
000
001
011
010
110
111
101
100

## Slide 11: BCD to Gray Code Converter
W = A + B D + B C
X = B C'
Y = B + C
Z = A'B'C'D + B C D + A D' + B' C D'
Minimized Functions:

## Slide 12: Example (Continued)
Notes:
4 product terms pre-assigned to each OR gates’ inputs
The OR gates’ inputs are internally pulled down by the manufacturer
A B C D
A
BD
BC
W X Y Z
BC’
B
C
BCD
AD’
BCD’

## Slide 13: PALs
Programmable Array Logic
  Realizes Sums of Products but with a fixed OR array

## Slide 14: PAL
inputs
1st output
section
2nd output
section
3rd output
section
4th output
section
Only functions with
at most four
products can be
implemented

## Slide 15: PAL
W = AB C  + CD
X = A BC  + A CD + ACD  + BCD
Y = A C D + ACD + A BD
x
x
x

## Slide 17: Helper Terms
  If an I/O pin’s output-control gate produces a constant 1,  the output is always enabled,
  The pin may be used as an input too.
  Outputs can be used to generate first-pass “helper terms” for logic functions that cannot be performed in a single pass with the limited number of AND terms available for a single output.