## Slide 1: Buffers
Buffer:
  Doesn’t change the input.
  Only amplifies.
in
out
EN

## Slide 2: Three-State Buffers
  Buffer output has 3 states: 0, 1, Z
  Z stands for High-Impedance  Open circuit
EN = 0  out = Z (open circuit)
EN = 1  out = in (regular buffer)
in
out
EN
EN | in | out
0 | X | Z
1 | 0 | 0
1 | 1 | 1

## Slide 3: Three-state buffer(BUF)/inverter(INV) symbols
in
out
EN
in
out
EN
in
out
EN
in
out
EN
3-state BUF, EN high
3-state BUF, EN low
3-state INV, EN low
3-state INV, EN high

## Slide 4: Open Collector/Drain Gates
  Outputs of two (or more) gates must not be wired together:
A
B
out
wired
If A = B
 out = A = B
If A  B
 a large enough current can be created, that causes excessive heating and could damage the circuit.

## Slide 5: Multiplexed output lines using three-state buffers
A
B
out
ENA
ENB
S
S | A | B | ENA | ENB | out
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1 | 1
1 | 1 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 1 | 1
A
B
A
B
S
out
0
1

## Slide 6: Open Collector/Drain Gates
  Outputs of some gates can be wired:
    The result: O1 AND O2
      Open Collector Gates in TTL Technology
      Open Drain Gates in CMOS Technology
A
B
Out =
O1
O2
O1 . O2

## Slide 7: Open Collector/Drain Gates
  Open Collector (Open Drain) NAND Truth Table:
A | B | F=(A•B)’
0 | 0 | Z
0 | 1 | Z
1 | 0 | Z
1 | 1 | 0
Z (Hi-Z) (Hi-Impedance):
  As if it is unconnected.
  The gate cannot pull up the output
     needs a resistor to pull it up if an input is ‘0’
OD

## Slide 8: Open Collector/Drain Gates
Wired AND:
If A and B are "1", output is actively pulled low
if C and D are "1", output is actively pulled low
if one gate is low, the other high, then low wins
if both gates are "1", the output floats, pulled
high by resistor
Hence, the two NAND functions are AND'd (wired)
together!
F
C
D
0 V
Open-collector
NAND gate
Pull-up resistor
OD
OD

## Slide 9: NAND-Only Implementation
  Find Sum-of-Product form.
  Inventers can be added
  Equivalent NAND-only

## Slide 10: NAND-Only Implementation
  NAND = AND + NOT
  Use Open Collector/Drain NAND Gates:
OD
OD
OD

## Slide 11: Another Method
  Instead of finding the circuit for F, find the circuit for F’ in the first stage
    Then there will be no Inverter at the output
Wired OR:
  Open drain/collector gate with active low inputs.
OD
OD
OD

## Slide 12: MOS Transistors

## Slide 13: CMOS Inverter

## Slide 14: CMOS NAND
Vdd
b
b
a
ab
gnd
a b ab
0 0
0 1
1 0
1 1
1
1
1
0

## Slide 15: CMOS NOR
Vdd
b
b
a
a+b
gnd
a b a+b
0 0
0 1
1 0
1 1
1
0
0
0

## Slide 16: CMOS XOR

## Slide 17: CMOS 3-State (Tri-State) Inverter

## Slide 19: Tri-State Buffer