## Slide 1: Microprocessors and Assembly Language Lecture 1 Hamed Farbeh farbeh@aut.ac.ir Fall 2024

## Slide 2: Course Description

## Slide 3: Grading
Final Exam: 40%
Midterm Exam : 30%
Homework: 10%
Project: 10%
Quizzes: 10%
AND
Lab

## Slide 4: Course Outline
Microprocessors and Microcontrollers
How they work
AND
How to work with them
Telegram channel: t.me/micro_fall2024

## Slide 5: References
Main
Arm Assembly Language Programming and Architecture, Volume 1, 1st edition, Muhammad Ali Mazidi, Sarmad Naimi, and Sepehr Naimi, MicroDigitalEd, 2013
Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15
ARMv7-M Architecture Reference Manual
Complementary material
ARM Assembly Language: Fundamentals and Techniques, 2nd Ed., William Hohl, Christopher Hinds, CRC Press, 2014.
Modern Assembly Language Programming with the ARM Processor, Larry D. Pyeatt, Elsevier, 2016.
Embedded Systems:Introduction to ARM®CORTEX-M Microcontrollers, Vol. 1, 5th Ed., Jonathan W. Valvano, 2014.

## Slide 6: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
Arm Assembly Language Programming and Architecture, Volume 1, 1st edition, Muhammad Ali Mazidi, Sarmad Naimi, and Sepehr Naimi, MicroDigitalEd, 2013
Design of Microprocessor-Based Systems (AKA Embeded Systems Design and Implementation), Prabal Dutta, University of Michigan
Cortex™-M3 Revision r2p1 Technical Reference Manual
ARMv7-M Architecture Reference Manual

## Slide 7: Computer History

## Slide 8: Computer History
Mechanical Computers (19th century)
Electro-Mechanical Computers (1936)
Electronic Computers (1941)

## Slide 9: Computer History
Mechanical Computers
  Abacus
  Mechanical calculators
    Pascal’s calculator (1642)
    Curta (1930s)
  Punched-card data processing (1725, 1800s, 1900s)

## Slide 10: Computer History
Mechanical Computers
  Difference engine: Charles Babbage (1791-1871)
    First general-purpose computing device
  Analytical engine

## Slide 11: Computer History
Electro-Mechanical Computers
  Switches, relays
  Early 1900s
  Zuse’s Z2, Z3, Z4
  (world's first commercial digital computer, mechanical memory)

## Slide 12: Computer History
Electronic Computers
  1st generation
    vacuum tubes (1945-1955)
    ENIAC, 1946

## Slide 13: Computer History
Electronic Computers
  2nd generation
    BJT transistors (1955-1965)
    CDC 6600 (1964-1969)
      world's fastest computer from 1964 to 1969
      $2,370,000
      30kW, 6tons
      10MHz, 2 MIPS
      Up to 982 kilobytes

## Slide 14: Computer History
Electronic Computers
  3rd generation
    integrated circuits (1965-1974)
    Intel 4004 (1971)
      The first commercially available microprocessor
      10 µm process
      92,000 instructions per second
      1 MHz clock rate
Major improvement of today's computers → better ICs.

## Slide 15: Computer History
Electronic Computers
  4th generation
    1974-1989
  5th generation: ULSI
    1990-present

## Slide 16: A brief recap of the computer history
Year | Technology Used in Computers | Relative Performance per unit cost
~1950 | Vacuum tube | 1
1960s | Transistor | 35
1975 | Integrated circuit | 900
1995 | Very large scale integrated circuit | 2,400,000
2005 | Ultra large scale integrated circuit | 6,200,000,000

## Slide 17: Computer History
What happened from 1970?
Transistor count doubles every 24-month

## Slide 18: Instruction Set Architecture (ISA)

## Slide 19: Instruction Set Architecture (ISA)
A set of instructions used by a machine to run programs
Interface between hardware & software
Computer language vocabulary
Provides an abstraction of hardware implementation
  Hardware implementation decides what and how
  instructions are implemented
ISA specifies
  Instructions, Registers,
  Memory access, Input/output
Applications
Compilers
Operating System
Architecture (ISA)
Microarchitecture
Digital Design
Circuit
Device
Layers of abstraction in the computer architecture

## Slide 20: Instruction Set Architecture (ISA)
How many instructions are needed?
What functionalities are required?
  Load/store
  Control
  Arithmetic/logic

## Slide 21: Instruction Set Architecture (ISA)
Key ISA decisions
  Instruction length
  Number, length, and types of registers
  Where operands reside
  How to access memory
  Instruction format
  Operand format: How many and how big

## Slide 22: Instruction Set Architecture (ISA)
Instruction length
Variable:
x86 – Instructions vary from 1 to 17 Bytes long
VAX – from 1 to 54 Bytes
MIPS, PowerPC, ARM:
all instruction are 4 Bytes long
Fixed:

## Slide 23: ISA: Instruction length
Variable-length instructions | Fixed-length instructions
Require multi-step fetch and decode | Allow easy fetch and decode
Allow for a more flexible and compact instruction set | Simplify pipelining and parallelism
CISC processors like x86 & VAX Complex Instruction Set Computing | RISC processors like MIPS & PowerPC Reduced Instruction Set Computing

## Slide 24: ISA: RISC vs. CISC
Early Trend
  Adding more instructions to next generation CPUs to do more complicated operations
  VAX arch had an instruction to multiply polynomials!
CISC Philosophy
  Limited main memory + immature compilers
    More dense instructions, highly encoded, variable length instructions
  Data loading as well as calculation

## Slide 25: ISA: RISC vs. CISC
RISC Philosophy
  Keep ISA small and simple
    Makes it easier to build faster hardware
  Let SW do complicated operations by composing simpler instructions
Note on “Reduced" in RISC Phrase
  Amount of work any single instruction accomplishes reduced
    Single ALU operation, single memory access, …

## Slide 26: ISA: RISC vs. CISC
CISC Problems
  Performance tuning challenging
    Complex/high-level instructions rarely used
  Slower clock rates
  Longer time-to-market
    Due to prolonged design time
CISC Features
  Ease compiler implementation
    HW supports all kind of addressing modes

## Slide 27: ISA: RISC vs. CISC
RISC Features
  Low complexity
    Less error-prone HW implementation
  Implementation advantages
    Less transistors
    Extra space: more registers, cache
  Marketing
    Reduced design time

## Slide 28: ISA: RISC vs. CISC
RISC vs. CISC
Hangul vs. Hiragana

## Slide 29: ISA: How many registers?
Advantages of a small number of registers
  Requires fewer bits to specify which one
  Less hardware
  Faster access
    Shorter wires
    Faster index decoding (fewer logic levels)
  Faster context switch (your OS course!)
    When all registers need saving
Faster access

## Slide 30: ISA: How many registers?
Advantages of a larger number of registers
  Fewer loads and stores needed
    Due to Less data transfer between CPU & memory
  Easier to do several operations at once

## Slide 31: ISA: Where do operands reside?
Stack Machine
  Generally outdated
Accumulator Machine
Register-Memory Machine
  Nowadays, computers are mainly from this category(Intel x86, Intel x64)
Load-Store Machine
  aka Register-Register Machine

## Slide 32: ISA: Where do operands reside?
Code sequence for C = A + B
Load-Store
1. Load R1, A
2. Load R2, B
3. Add R3, R1, R2
4. Store C, R3
Accumulator
1. Load A
2. Add B
3. Store C
Register-Memory
1. Add C, A, B
Stack
1. Push A
2. Push B
3. Add
4. Pop C

## Slide 33: Harvard vs. Von Neumann

## Slide 34: Types of Computer Systems

## Slide 35: Types of Computer Systems
Desktops
  General purpose
  Market dominated by x86 processors
  Various software
  For use by individuals
Servers and Warehouse-Scale Computers (WSCs)
  Thousands of cores and disks
  Market dominated by x86-compatible server chips
  Dedicated apps, plus cloud hosting of virtual machines
  Increasing use of GPUs, FPGAs, and custom hardware to accelerate workloads

## Slide 36: Types of Computer Systems
Mobile (smartphone/tablet)
    >1 billion sold/year
    Market dominated by ARM-ISA-compatible general-purpose processor in system-on-a-chip (SoC)
    Plus sea of custom accelerators (radio, image, video, graphics, audio, motion, location, security, etc.)
  Anything Else?

## Slide 37: Types of Computer Systems
Embedded Systems

## Slide 38: Computer System Design Criteria
Implementation cost Time to market Maintainability Debugging Flexibility Scalability … | Performance Power consumption Energy consumption Area Weight Design cost

## Slide 39: Options for Building Embedded Systems
Dedicated hardware
  ASIC (Application-specific integrated circuit)
    Hard to implement a dedicated hardware from scratch
    There is only a limited number of hardware producers
  Programmable logic (FPGA, PLD)
  -> Both methods are costly and complicated
Software running on generic hardware
  Microprocessor + memory + peripherals
  Microcontroller (internal memory & peripherals)
A combination of all options (Complex systems)

## Slide 40: Microprocessor vs. Microcontroller
Microprocessor
  An IC that has only CPUs inside it
  No RAM, ROM, or other peripheral
Microcontroller (MCU)

## Slide 41: Microprocessor vs. Microcontroller
Microprocessor
Microcontroller (MCU)

## Slide 42: Microprocessor vs. Microcontroller
Microprocessor | Microcontroller
Heart of computer systems | Heart of embedded systems
It is just a processor. Memory and I/O components are connected externally | Has processor along with internal memory and I/O components
Since memory and I/O have to be connected externally, the circuit becomes larger | Since memory and I/O have to be connected externally, the circuit is small
Cannot be used in compact system | It is efficient for compact systems
The entire energy consumption is high due to external components | Suitable for battery-operated systems
Slow memory access | Fast memory access
Is based on Von Neumann architecture (program and data are stored in the same memory module) | Is based on Harvard architecture (program and data memory are separate)