## Slide 1: Microprocessors and Assembly Language Lecture 14 Hamed Farbeh farbeh@aut.ac.ir Fall 2024

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
Arm Assembly Language Programming and Architecture, Volume 1, 1st edition, Muhammad Ali Mazidi, Sarmad Naimi, and Sepehr Naimi, MicroDigitalEd, 2013.

## Slide 3: HLL Advantages over assembly
More user friendly
Provide a better user interface
Helps programmers use a more modular approach
Are easier and faster to code and debug
Increases the programmer’s productivity
Is machine independent
English statements are used
Easy to debug
Easy to maintain program

## Slide 4: Why to Learn Assembly Language
Writing assembly code is desirable or necessary for
  The first steps in booting the computer
  Code to handle interrupts
  Low-level locking code for multi-threaded programs
  Code for machines where no compiler exists
  Code which needs to be optimized beyond the limits of the compiler
  On computers with very limited memory
  Code that requires low-level access to architectural and/or processor features
  Write a compiler
  Program device drivers

## Slide 5: ARM Architecture and Assembly Language Programming

## Slide 6: SUB Instruction
We have already seen MOV and ADD instr.
SUB Rd, Rn, Op2 ; Rd = Rn – Op2
A simple code
MOV R1, #0x34 ; load 0x34 into R1 (R1 = 0x34) SUB R5, R1, #0x25 ; R5 = R1 – 0x25 (R5 = 0x34 – 0x25)
Arm uses 2’s complement for negative numbers

## Slide 7: ALU Instructions Using GPRs

## Slide 8: The ARM Memory Map
Memory space allocation in the ARM
  4 gigabytes of directly accessible memory space
from 0 to 0xFFFFFFFF
Memory space can be divided into five sections
  On-chip peripheral and I/O registers
  On-chip data SRAM
  On-chip EEPROM (for saving critical data)
  On-chip Flash ROM (program space)
  Off-chip DRAM space

## Slide 9: The ARM Memory Map
Why both EEPROM and Flash?
Why both SRAM and EEPROM?
IO-mapped or Memory-Mapped IO?
Memory space is 4GB; is it enough?

## Slide 10: The ARM Memory Map
Q: A given ARM chip has the following address assignments. Calculate the space and the amount of memory given to each section.
(a) Address range of 0x00100000 – 0x00100FFF for EEPROM
(b) Address range of 0x40000000 – 0x40007FFF for SRAM
(c) Address range of 0x00000000 – 0x0007FFFF for Flash
(d) Address range of 0xFFFC0000 – 0xFFFFFFFF for peripherals