## Slide 1: Microprocessors and Assembly Language Lecture 15 Hamed Farbeh farbeh@aut.ac.ir Fall 2024

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
  Arm Assembly Language Programming and Architecture, Volume 1, 1st edition, Muhammad Ali Mazidi, Sarmad Naimi, and Sepehr Naimi, MicroDigitalEd, 2013.

## Slide 3: Load and Store Instructions
Load Rd with the contents of location pointed to by Rx register
LDR Rd,[Rx]; Rx contains an address between 0x00000000 to 0xFFFFFFFF
LDR reads one word (32-bit or 4-byte) of data
  from 4 consecutive memory locations
  The locations can be in the SRAM, a Flash memory or I/O registers

## Slide 4: Load and Store Instructions
Store register Rd into locations pointed to by Rx
STR Rd,[Rx]

## Slide 5: Load and Store Variations
Load a byte
LDRB Rd, [Rx]

## Slide 6: Load and Store Variations
Store a byte
STRB Rd, [Rx]

## Slide 7: Load and Store Variations
Load half-word (2-byte)
LDRH Rd, [Rx]

## Slide 8: Load and Store Variations
Store half-word (2-byte)
STRH Rd, [Rx]

## Slide 9: LDR, STR and MOV comparison
LDR: moves data from memory to processor. loads data to a specified register.
STR: moves data out of the processor to a memory location from a specified register.
Note: Both of the instructions above can use various addressing modes allowed by ARM, while specifying address of the memory location (indirect addressing, PC-relative, displacement etc.)
MOV: copies from register to register, or loads a constant into a register.

## Slide 10: Current Program Status Register
CPSR: Flag register
N: Negative
Z: Zero
C: Carry
V: Overflow
T: Thumb
I and F: Enable or disable the interrupt

## Slide 11: S suffix and the status register
By executing data processing instructions
  By default, the status flags of CPSR are not updated
To update the flags
  put the ‘S’ suffix at the end of the opcode
ADD => ADDS

## Slide 12: S Suffix and the Status Register

## Slide 13: Flag Bits and Decision Making
Conditional branch instructions

## Slide 14: Question
Write a program to see if a given number (in this example 0x80000001) is palindrome.

## Slide 15: Answer
Mov R0, 0x80000001
Mov R1, R0
Mov R2, #0
Mov R3, #32 ; loop counter
Mov R4, #0 ; output
Loop
AND R5,R1,#1
LSL R2,R2,#1
ADD R2,R2,R5
LSR R1,R1,#1
SUBS R3,R3,#1
BNE Loop
CMP R0,R2
BNE Here
MOV R4,#1
Here B Here
Ex: 1001 is a 4-bit palindrome