## Slide 1: Microprocessors and Assembly Language Lecture 16 Hamed Farbeh farbeh@aut.ac.ir Fall 2024

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
  Arm Assembly Language Programming and Architecture, Volume 1, 1st edition, Muhammad Ali Mazidi, Sarmad Naimi, and Sepehr Naimi, MicroDigitalEd, 2013.

## Slide 3: ARM Data Format, Pseudo-instructions and Directives

## Slide 4: ARM Data Format
Data format representation
  Hexadecimal numbers
MOV R1, #0x99
  Decimal numbers
MOV R7, #12
  Binary numbers
  MOV R6, #2_10011001
  Numbers in any base between 2 and 9
  MOV R7, #8_33
  ASCII characters
  LDR R3, #'2' ; R3 = 00110010 or 32 in hex

## Slide 5: Pseudo-instructions
The ARM assembler supports a number of pseudo-instructions. At assembly time they are translated into the appropriate combination of ARM instructions.
LDR pseudo-instruction
  Limitation of loading immediate value: 8-bit
MOV Rd, 0x11223344
LDR Rd, =32-bit_immediate_value
LDR R7, =0x11223344
Load registers with the addresses of memory locations
ADR Rn, label

## Slide 6: Assembler Directives
Directives give directions to the assembler
  Some Widely Used ARM Directive

## Slide 7: Assembler Directives
Directives: AREA
  Defines a new section of memory
AREA section name, attribute, attribute, ...
Some attributes: CODE, DATA, READONLY, READWRITE, and ALIGN
AREA MY_ASM_PROG1, CODE, READONLY

## Slide 8: Assembler Directives
Directives: AREA
  Attributes: READONLY
    All the READONLY sections of the same program are put next to each other in the flash memory by the linker
  Attributes: READWRITE
    The linker puts all the READWRITE sections of the same program next to each other in the SRAM memory
  Attributes: CODE: is by default READONLY memory
  Attributes: DATA: is by default READWRITE memory
  Attributes: ALIGN: to align a section

## Slide 9: Assembler Directives
Directives: END
  Indicates to the assembler the end of the source code
  Is the last line of the ARM assembly program
    Anything after the END directive in the source file is ignored by the assembler
AREA PROG_2_1, CODE, READONLY MOV R1, #0x25 ; R1 = 0x25 MOV R2, #0x34 ; R2 = 0x34 ADD R3, R2, R1 ; R3 = R2 + R1
HERE B HERE ; stay here forever
END