## Slide 1: Microprocessors and Assembly Language Lecture 19 Hamed Farbeh farbeh@aut.ac.ir Fall 2024

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
Arm Assembly Language Programming and Architecture, Volume 1, 1st edition, Muhammad Ali Mazidi, Sarmad Naimi, and Sepehr Naimi, MicroDigitalEd, 2013.

## Slide 3: Arithmetic and Logic Instructions and Programs

## Slide 4: Arith. Instr. and Flag Bits for Unsigned Data
No increment instr. In ARM
  Use the available ADD instr.

## Slide 5: ADD and ADC
Add
    ADD Rd, Rn, Op2 ; Rd = Rn + Op2
    LDR R0, =0x10; R0 = 0x10
    ADD R1, R0, 0x5; R1 = 0x15
Add with carry
ADC Rd, Rn, Op2; Rd = Rn + Op2 + Carry

## Slide 6: Multiword ADD
Add 0x35F62562FA to 0x21F412963B
      LDR R0, =0xF62562FA; R0 = 0xF62562FA
      LDR R1, =0xF412963B; R1 = 0xF412963B
      MOV R2, #0x35; R2 = 0x35
      MOV R3, #0x21; R3 = 0x21
      ADDS R5, R1, R0; R5 = 0xF62562FA + 0xF412963B ; now C = 1
      ADC R6, R2, R3; R6 = R2 + R3 + C; = 0x35 + 21 + 1 = 0x57

## Slide 7: SUB and SBC
Subtract
    ADD Rd, Rn, Op2; Rd = Rn + Op2
    LDR R0, =0x10; R0 = 0x10
    SUB R1, R0, 0x5; R1 = 0x0B
Subtract with carry
    SBC Rd, Rn, Op2
    ; Rd = Rn - Op2 - !Carry
    ; Subtracts 1 from the result if carry is not set

## Slide 8: Multiword SUB
Sub 0x21F62562FA from 0x35F412963B
  LDR R0, =0xF62562FA; R0 = 0xF62562FA ; notice the syntax for LDR
  LDR R1, =0xF412963B; R1 = 0xF412963B
  MOV R2, #0x21; R2 = 0x21
  MOV R3, #0x35; R3 = 0x35
  SUBS R5, R1, R0; R5 = R1 – R0; = 0xF412963B – 0xF62562FA, and C = 0
  SBC R6, R3, R2; R6 = R3 – R2 – 1 + C; = 0x35 – 0x21 – 1 + 0 = 0x13

## Slide 9: Multiplication and Division of Unsigned Numbers
Not all CPUs have instr. for mult. and div.
  All the ARM processors have mult., but not all have div.
  ARM Cortex-M3 and M4 have both mult. and div.
MUL: Regular multiplication
MULL: long multiplication

## Slide 10: Multiplication of Unsigned Numbers
MUL: Regular multiplication
MULL: long multiplication
    LDR R1, =100000; R1=100,000
    LDR R2, =150000; R2=150,000
    MUL R3, R2, R1; R3 is not 15,000,000,000; it cannot fit in 32 bits.
    LDR R1, =0x54000000; R1 = 0x54000000
    LDR R2, =0x10000002; R2 = 0x10000002
    UMULL R3, R4, R2, R1; 0x54000000 × 0x10000002 = 0x054000000A8000000;
    ; R3 = 0xA8000000, the lower 32 bits R4 = 0x05400000, the higher 32 bits

## Slide 11: Multiplication of Unsigned Numbers
Multiply and Accumulate Instructions in ARM
    MLA Rd, Rm, Rs, Rn ; Rd = Rm × Rs + Rn MOV R1, #100; R1 = 100
    MOV R2, #5; R2 = 5
    MOV R3, #40; R3 = 40
    MLA R4, R1, R2, R3; R4 = R1 × R2 + R3 = 100 × 5 + 40 = 540
To accumulate the products of the multiplication
    MLA R3, R1, R2, R3; R3 = R1 × R2 + R3 or R3 += R1 × R2
UMLAL: unsigned multiply and accumulate long
    UMLAL RdLo, RdHi, Rn, Op2; RdHi:RdLo = Rn × Op2 + RdHi:RdLo

## Slide 12: Bitwise operations
Bitwise AND
AND Rd, Rn, Op2 AND R0, R1, #0xF0; R0 = R1 & 0xF0
Bitwise OR
ORR Rd, Rn, Op2 ORR R0, R1, #0x10; R0 = R1 | 0x10
Bitwise XOR
EOR Rd, Rn, Op2 EOR R0, R1, #0xFF; R0 = R1 ^ 0xFF (Same as a bitwise NOT)
Bitwise NOT
MVN Rd, Op2 MVN R1, R1; R1 != R1

## Slide 13: Rotate and Barrel Shifter
LSR: Logical shift right
    MOV R0, #0x9A; R0 = 0x9A
    MOVS R1, R0, LSR #3
    ; shift right R0 3 times, then store the result in R1 MOV R0, #0x9A
    MOV R2, #0x03
    MOVS R1, R0, LSR R2
    ; shift right R0 R2 times; and move the result to R1

## Slide 14: Rotate and Barrel Shifter
LSL: Logical shift left
MOV R1, R1, LSL R2
ROR: Rotate right
MOVS R1, R1, ROR #1
MOVS R1, R1, ROR R0

## Slide 15: Rotate and Barrel Shifter
NO ROL: Rotate left
  Use ROR for rotating left
  n-bit ROL ⬄ (32 - n)-bit ROR
    Take care of carry
RRX: Rotate right through carry
  Takes no arguments
    MOVS R2, R2, RRX; Rotate 1 bit

## Slide 16: Rotating Immediate Arguments
MOV Instruction
MOV R0, #0xFF, #2; R0 = 0xFF is rotated right 2 times. R0 = 0xC000003F
MOV R0, #0xFF, #12; R0 = 0xFF is rotated right 12 times. R0 = 0x0FF00000
MOV R0, #0xFF, #28; R0 = 0xFF is rotated right 28 times. R0 = 0x00000FF0
BUT, Rotate field (bit11-bit8) is 4-bit

## Slide 17: Rotating Immediate Arguments
Shift instruction
MOV R0, R2, LSL #8 ⬄ LSL R0, R2, #8
ASR: Arithmetic Shift right
ASR Rd, Rm, Rn
ASRS Rd, Rm, Rn
LSL: Logical Shift Left
LSL Rd, Rm, Rn
…

## Slide 18: Rotating Immediate Arguments
The multiplication instruction can take 32 clock cycles in some systems
Shifting and adding could be used in some cases instead
MUL R0, R0, #9; R0 *= 9 ADD R0, R0, R0, LSL #3; R0 = R0 + R0*8

## Slide 19: Reverse Subtraction
SUB: Rd = Rn – Op2
You can only shift or use an immediate value in the second operand.
What if you want to subtract a register from an immediate value or a shifted register?
Reverse Subtraction:
  RSB Rd, Rn, Op2; Rd = Op2 – Rn

## Slide 20: BCD and ASCII Conversion
Unpacked BCD: each decimal digit is represented by a byte
0000 1001 0000 0101 ⬄ 95
Packed BCD: two decimal digits are packed in one byte
1001 0101 ⬄ 95
Ex: Decimal 452 in packed and unpacked BCD
  Packed: 0100 0101 0010
  Unpacked 0000 0100 0000 0101 0000 0010

## Slide 21: BCD and ASCII Conversion
ASCII to unpacked BCD conversion
  Get rid of the "011" in the upper 3 bits of the 7-bit ASCII
    ASCII number is ANDed with "0000 1111“
LDR R0, =0x35; ASCII code for ‘5’
AND R0, R0, #0xF; Remove the 0110 in the upper 4 bits, R0 = 0000 0101

## Slide 22: BCD and ASCII Conversion
ASCII to packed BCD conversion
  First convert to unpacked BCD (remove the upper 3 bits)
  Combine every two digits to make a packed BCD
  LDR R0, =0x34; ASCII code for ‘4’
  LDR R1, =0x35; ASCII code for ‘5’
  AND R0, R0, #0xF; R0 = 0000 0100
  AND R1, R1, #0xF; R1 = 0000 0101
  ORR R2, R0, R1, LSL #4; R2 = 0101 0100

## Slide 23: BCD and ASCII Conversion
Packed BCD to ASCII conversion
  Convert packed BCD to unpacked BCD
  Tagged with 011 0000 (0x30)

## Slide 24: Question
In the least significant 8 bits of R0, there are two decimal digits encoded as Packed BCD.
Write a program to decode and put these two digits in R1 and R2. If these two digits form a single 2-digit integer, compute and put the integer in R3.
Rewrite the above program with at most 5 instructions and without using multiplication instructions.

## Slide 25
End of Chapter 3!