## Slide 1: Microprocessors and Assembly Language Lecture 3 Hamed Farbeh farbeh@aut.ac.ir Fall 2024

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 3: SAM3X8E Specifications

## Slide 4: Configuration Summary

## Slide 6: Recap
Harvard architecture
Memory to store data
SRAM, volatile
Memory to store instructions
FLASH, non- volatile

## Slide 7: SAM3X8E Operating Modes
Active Mode
  Normal running mode with the core clock running from the fast RC oscillator
Low Power Modes
  Embedded systems are reactive
  Backup Mode
  Wait Mode
  Sleep Mode

## Slide 8: SAM3X8E Operating Modes
Low Power Modes
  Backup Mode
    Achieve the lowest power consumption possible in a system
    For tasks not requiring fast startup time (< 0.5 ms)
    The core is off
    Note that peripherals responsible for detecting and handling interrupts are not off
  Wait Mode
    Very low power while maintaining the whole device in a powered state for a startup time of less than 10 µs
    The clocks of the core, peripherals and memories are stopped
    The core, peripherals, and memories power supplies are still powered
  Sleep Mode
    Only the core clock is stopped
    Example: Direct Memory Access (DMA)

## Slide 9: SAM3X8E Input/Output Lines
General Purpose I/O Lines (GPIO)
  Managed by Parallel Input/Output (PIO) Controllers
  I/O Modes:
    Pull-up
    Input Schmitt triggers
    Multi-drive (open-drain)
    Glitch filters
    Debouncing
    Input change interrupt

## Slide 10: I/O Modes
Pull-up
output lines are usually pull-up
example: telephone lines

## Slide 11: I/O Modes
Input Schmitt triggers
usually used for input lines
example: water heater

## Slide 12: I/O Modes
Multi-drive (open-drain)
both input and output lines can be open-drain

## Slide 13: I/O Modes
Glitch filters

## Slide 14: I/O Modes
Debouncing

## Slide 15: I/O Modes
Input change interrupt

## Slide 16: SAM3X8E Input/Output Lines
System I/O Lines
  Shared with PIO lines
NRST Pin
  Handled by the on-chip reset controller (bidirectional)
  Provides a reset signal to the external components
  Is asserted low externally to reset the microcontroller
NRSTB Pin
  Asynchronous reset of the SAM3X/A series when asserted low
ERASE Pin
  Reinitialize the Flash content to an erased state

## Slide 17: SAM3X8E External Memories
External Memory Bus
  Integrates Four External Memory Controllers
    Static Memory Controller
    NAND Flash Controller
    SLC NAND Flash ECC Controller
    Single Data Rate Synchronous Dynamic Random Access Memory (SDR-SDRAM)
  Up to 24-bit Address Bus (up to 16 Mbytes linear per chip select)
  Up to 8 chip selects, Configurable Assignment

## Slide 18: Real-time Timer (RTT)
A 32-bit counter
For counting elapsed seconds
Generates a periodic interrupt and/or triggers an alarm
Real-time Timer Value Register
  Name: RTT_VR
  Address: 0x400E1A38
  Access: Read-only

## Slide 19: Real-time Clock (RTC)
RTC peripheral is designed for very low power consumption
Combines a complete time-of-day clock with alarm and a 200-year Gregorian calendar
Programmable periodic interrupt

## Slide 20: Watchdog Timer (WDT)
Used to prevent system lock-up
  If the software becomes trapped in a deadlock
  Is loaded with an initial value greater than the worst case time delay
  If not reinitialized before reaching 0
    An interrupt is generated to reset the processor
A 12-bit down counter
  Watchdog period of up to 16 seconds

## Slide 21: The End!