## Slide 1: Microprocessors and Assembly Language Lecture 8 Hamed Farbeh farbeh@aut.ac.ir Fall 2024

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
Arm Assembly Language Programming and Architecture, Volume 1, 1st edition, Muhammad Ali Mazidi, Sarmad Naimi, and Sepehr Naimi, MicroDigitalEd, 2013
Design of Microprocessor-Based Systems (aka Embedded Systems Design and Implementation), Prabal Dutta, University of Michigan
CortexTM-M3 Revision r2p1 Technical Reference Manual
ARMv7-M Architecture Reference Manual

## Slide 3: I2C-bus specification

## Slide 4: I2C Description
Synchronous serial data link
  Multi-master, multi-slave (Unlike SPI which is single-master, multi-slave)
  Invented in 1982 by Philips Semiconductor (now NXP Semiconductors)
  Widely used for attaching lower-speed peripheral ICs to processors and microcontrollers in short-distance (Somewhat similar to SPI)
  Appropriate for peripherals where simplicity and low manufacturing cost are more important than speed (Somewhat similar to SPI)
https://en.wikipedia.org/wiki/I%C2%B2C

## Slide 5: I2C Design
Two bidirectional open collector or open drain lines (SPI has four communication lines)
  open collector (or open drain): behaves like a switch that is either connected to ground or disconnected
  Serial Data Line (SDA) and Serial Clock Line (SCL)
pulled up with resistors (They always have a value of one when there is no data)
7-bit address space (rarely-used 10-bit extension) (Through Serial Data Line)
Each device has an address
The master is responsible for managing the communication and specifies the beginning and the end of the communication
https://en.wikipedia.org/wiki/I%C2%B2C

## Slide 6: I2C Design
Bus speeds
  100 kbit/s: standard mode
  400 kbit/s: Fast mode
  10 kbit/s: low-speed mode
  1 Mbit/s: Fast mode plus
  3.4 Mbit/s: High Speed mode
  5 Mbit/s Ultra Fast-mode
https://en.wikipedia.org/wiki/I%C2%B2C

## Slide 7: I2C Design
Operating roles
  Master: generates the clock and initiates communication with slaves
  Slave: receives the clock and responds when addressed by the master
Multi-master bus: any number of master nodes can be present but it can only have one master at the moment
Master and slave roles may be changed between messages (Communication is always between a master and a slave)
https://en.wikipedia.org/wiki/I%C2%B2C

## Slide 8: I2C Design (Different modes of a node)
Each node is either a transmitter or a receiver at the moment
Potential modes of operation for a given bus device
  Master transmit – master node is sending data to a slave
  Master receive – master node is receiving data from a slave
  Slave transmit – slave node is sending data to the master
  Slave receive – slave node is receiving data from the master
https://en.wikipedia.org/wiki/I%C2%B2C

## Slide 9: I2C Data Transfer
Message delimiters
  START and STOP signals (Master generates)
  Are distinct from the data bits (0 and 1)
The master is initially in master transmit mode by sending a START (Write a zero on the data line) followed by the 7-bit address of the slave
  followed by a single bit representing whether it wishes to write (0) to or read (1) from the slave
The slave will respond with an ACK bit (active low (why?) for acknowledged)
  If slave exists and is ready to communicate
The address and the data bytes are sent most significant bit first
https://en.wikipedia.org/wiki/I%C2%B2C

## Slide 10: I2C Data Transfer
The start bit is indicated by a high-to-low transition of SDA
  with SCL high
The stop bit is indicated by a low-to-high transition of SDA
  with SCL high
All other transitions of SDA take place with SCL low
To write to the slave
  The Master repeatedly sends a byte with the slave sending an ACK bit
To read from slave
  Master repeatedly receives a byte from the slave, and send an ACK bit after every byte except the last one
https://en.wikipedia.org/wiki/I%C2%B2C

## Slide 11: I2C Data Transfer

## Slide 12: Two-wire Interface (TWI)
I2C-Compatible interface of ATMEL microcontroller
  Two GPIO pins should be configured
  speeds of up to 400 Kbits/s
It can have 128 devices ()
Chapter 33: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 13: Clock Stretching
In an I2C communication, the master device determines the clock speed.
There are situations where an I2C slave is not able to co-operate with the clock speed given by the master and needs to slow down a little.
This is done by a mechanism referred to as “clock stretching” which allows it to work with these different clocks.
But HOW?!
https://www.i2c-bus.org/clock-stretching/

## Slide 14: Clock Stretching
It is possible for a slave device to hold the SCL signal low (0), which “stretches” the clock and can halt the master device from transmitting data or commands.
The master, on the other hand, is required to read back the clock signal after releasing it to the high state and wait until the line has actually gone high.
As a result, this method solves the problem of different clocks

## Slide 15: The End (for now)!