## Slide 1: Microprocessors and Assembly Language Lecture 9 Hamed Farbeh farbeh@aut.ac.ir Fall 2024

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
Arm Assembly Language Programming and Architecture, Volume 1, 1st edition, Muhammad Ali Mazidi, Sarmad Naimi, and Sepehr Naimi, MicroDigitalEd, 2013
Design of Microprocessor-Based Systems (AKA Embeded Systems Design and Implementation), Prabal Dutta, University of Michigan
Cortex™-M3 Revision r2p1 Technical Reference Manual
ARMv7-M Architecture Reference Manual

## Slide 3: Universal Asynchronous Receiver/Transmitter (UART)

## Slide 4: Introduction to UART
Remember when printers, mice, and modems had thick cables with those huge clunky connectors? The ones that literally had to be screwed into your computer? Those devices were probably using UARTs to communicate with your computer. While USB has almost completely replaced those old cables and connectors, UARTs are definitely not a thing of the past. You’ll find UARTs being used in many DIY electronics projects to connect GPS modules, Bluetooth modules, and RFID card reader modules to your Raspberry Pi, Arduino, or other microcontrollers.

## Slide 5: Introduction to UART
UART stands for Universal Asynchronous Receiver/Transmitter. It’s not a communication protocol like SPI and I2C, but a physical circuit in a microcontroller, or a stand-alone IC. A UART’s main purpose is to transmit and receive serial data.

## Slide 6: Basics of UART Communication
Asynchronous serial communication
  Uses two wires to transmit data between devices
  Data flows from the Tx pin of the transmitting UART
    to the Rx pin of the receiving UART
  No clock signal to synchronize the output of bits from the transmitting UART
    to the sampling of bits by the receiving UART
http://www.circuitbasics.com/basics-uart-communication/

## Slide 7: UART Communication Details
The transmitting UART adds start and stop bits
  to the data packet being transferred
These bits define the beginning and end of the data packet
  so the receiving UART knows when to start reading the bits
The receiving UART detects a start bit
  Then, starts to read the incoming bits
    at a specific frequency known as the baud rate
Baud rate: a measure of the speed of data transfer
  expressed in bits per second (bps)
The baud rate between the transmitting and receiving UARTs can only differ by about 10%
http://www.circuitbasics.com/basics-uart-communication/

## Slide 8: UART Communication Details
Data Transmission
  In UART, the mode of transmission is in the form of a packet. The piece that connects the transmitter and receiver includes the creation of serial packets and controls those physical hardware lines. A packet consists of a start bit, data frame, a parity bit, and stop bits.

## Slide 9: UART Communication Details
START BIT
  The transmitting UART pulls the line from high to low for one clock cycle
  The UART data transmission line is normally held at a high voltage level when it’s not transmitting data. To start the transfer of data, the transmitting UART pulls the transmission line from high to low for one (1) clock cycle. When the receiving UART detects the high-to-low voltage transition, it begins reading the bits in the data frame at the baud rate frequency

## Slide 10: UART Communication Details
Data Frame
  The data frame contains the actual data being transferred. It can be five (5) bits up to eight (8) bits long if a parity bit is used. If no parity bit is used, the data frame can be nine (9) bits long. In most cases, the data is sent with the least significant bit first.

## Slide 11: UART Communication Details
Parity
  Parity describes the evenness or oddness of a number. The parity bit is a way for the receiving UART to tell if any data has changed during transmission. Bits can be changed by electromagnetic radiation, mismatched baud rates, or long-distance data transfers.

## Slide 12: UART Communication Details
Parity
  After the receiving UART reads the data frame, it counts the number of bits with a value of 1 and checks if the total is an even or odd number. If the parity bit is a 0 (even parity), the 1 or logic-high bit in the data frame should total to an even number. If the parity bit is a 1 (odd parity), the 1 bit or logic highs in the data frame should total to an odd number.
  When the parity bit matches the data, the UART knows that the transmission is free of errors. But if the parity bit is a 0, and the total is odd, or the parity bit is a 1, and the total is even, the UART knows that bits in the data frame have changed.

## Slide 13: UART Communication Details
Stop Bits
  To signal the end of the data packet, the sending UART drives the data transmission line from a low voltage to a high voltage for one (1) to two (2) bit(s) duration.

## Slide 14: UART in SAM3X8E
Independent Receiver and Transmitter
  with a Common Programmable Baud Rate Generator
Even, Odd, Mark or Space Parity Generation
Parity, Framing and Overrun Error Detection
Interrupt Generation
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 15: UART in SAM3X8E
The UART pins are multiplexed with PIO lines
The programmer must first configure the PMC to enable the UART clock
  PMC: Power Management Controller
Only 8-bit character is supported (with parity)
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 16: Baud Rate Generator in SAM3X8E
The baud rate clock
  Is the master clock divided by 16 times the value (CD) written in UART_BRGR (Baud Rate Generator Register)
  If UART_BRGR is set to 0, the baud rate clock is disabled and the UART remains inactive
The maximum allowable baud rate is Master Clock divided by 16
The minimum allowable baud rate is Master Clock divided by (16 x 65535)
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 17: Baud Rate Generator in SAM3X8E
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 18: UART Receiver in SAM3X8E
Receiver Reset, Enable and Disable
  After the device reset, the UART receiver is disabled
  To enable: RXEN = 1 in the control register (UART_CR)
  If enabled: the receiver starts looking for a start bit
  To disable: RXDIS = 1 in the control register (UART_CR)
    If the receiver is waiting for a start bit, it is immediately stopped
    If the receiver has already detected a start bit and is receiving the data, it waits for the stop bit before actually stopping its operation
  To reset: RSTRX =1 in the control register (UART_CR)
    The receiver immediately stops its current operations and is disabled, whatever its current state!
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 19: Start Detection and Data Sampling
A low level (space) on URXD is interpreted as a valid start bit
  if it is detected for more than 7 cycles of the sampling clock
  Sampling clock = 16 x baud rate
The receiver samples the URXD at the theoretical midpoint of each bit
  When a valid start bit has been detected
  It is assumed that each bit lasts 16 cycles of the sampling clock (1-bit period): the bit sampling point is eight cycles (0.5-bit period) after the start of the bit
  The first sampling point is, therefore 24 cycles (1.5-bit periods) after the falling edge of the start bit was detected
Each subsequent bit is sampled 16 cycles (1-bit period) after the previous one
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 20: Start Detection and Data Sampling
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 21: Receiver Ready
When a complete character is received
  Is transferred to the receive holding register (UART_RHR )
  The RXRDY status bit in UART_SR (Status Register) is set
  The bit RXRDY is automatically cleared when the UART_RHR is read
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 22: Receiver Overrun
If UART_RHR has not been read by the software (or the Peripheral Data Controller or DMA Controller) since the last transfer
  and a new character is received
    the OVRE status bit in UART_SR is set
OVRE is cleared when the software writes the control register UART_CR with the bit RSTSTA (Reset Status) at 1
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 23: Transmitter
The UART transmitter is disabled after the device reset
  To enable: TXEN = 1 in the control register UART_CR
    The transmitter waits for a character to be written in the Transmit Holding Register (UART_THR) before actually starting the transmission
  To disable: TXDIS = 1 in the control register UART_CR
    If the transmitter is not operating, it is immediately stopped
    If a character is being processed into the Shift Register and/or a character has been written in the Transmit Holding Register, the characters are completed before the transmitter is stopped
  To reset: RSTTX = 1 in the UART_CR
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 24: Transmitter Control
When enabled, the bit TXRDY is set in the UART_SR
The transmission starts when
  The programmer writes in the UART_THR and
  The written character is transferred from UART_THR to the Shift Register
  The TXRDY bit remains high until a second character is written in UART_THR
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 25: Transmitter Control
As soon as the first character is completed
  The last character written in UART_THR is transferred into the shift register and TXRDY rises again
    Showing that the holding register is empty
When both the Shift Register, and UART_THR are empty
  All the characters written in UART_THR have been processed
  The TXEMPTY bit rises after the last stop bit has been completed
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 26: Transmitter Control
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 27: Steps of UART Transmission(Summary)
First: The transmitting UART receives data in parallel from the data bus.
Second: The transmitting UART adds the start bit, parity bit, and the stop bit(s) to the data frame.
Third: The entire packet is sent serially starting from start bit to stop bit from the transmitting UART to the receiving UART. The receiving UART samples the data line at the preconfigured baud rate.
Fourth: The receiving UART discards the start bit, parity bit, and stop bit from the data frame.
Fifth: The receiving UART converts the serial data back into parallel and transfers it to the data bus on the receiving end.

## Slide 28: Steps of UART Transmission(Summary)
27

## Slide 29: UART Registers
UART Control Register: UART_CR
  RSTRX: Reset Receiver
  RSTTX: Reset Transmitter
  RXEN: Receiver Enable
  RXDIS: Receiver Disable
  TXEN: Transmitter Enable
  TXDIS: Transmitter Disable
  RSTSTA: Reset Status Bits (Resets the status bits PARE, FRAME and OVRE in the UART_SR)
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 30: UART Registers
UART Mode Register: UART_MR
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 31: UART Registers
UART Interrupt Enable Register: UART_IER
  RXRDY: Enable RXRDY Interrupt
  TXRDY: Enable TXRDY Interrupt
  ENDRX: Enable End of Receive Transfer Interrupt
  ENDTX: Enable End of Transmit Interrupt
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15
  OVRE: Enable Overrun Error Interrupt
  FRAME: Enable Framing Error Interrupt
  PARE: Enable Parity Error Interrupt
  TXEMPTY: Enable TXEMPTY Interrupt
  TXBUFE: Enable Buffer Empty Interrupt
  RXBUFF: Enable Buffer Full Interrupt

## Slide 32: UART Registers
UART Receiver Holding Register: UART_RHR
  Read-only
  RXCHR: Received Character
    Last received character if RXRDY is set
UART Transmit Holding Register: UART_THR
  Write-only
  TXCHR: Character to be Transmitted
  Next character to be transmitted after the current character if TXRDY is not set
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 33: UART Registers
UART Baud Rate Generator Register: UART_BRGR
  CD: Clock Divisor
  0 = Baud Rate Clock is disabled
  1 to 65,535 = MCK / (CD x 16)
Ch. 34: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 34: The End!